## Slide 1: Hydrology of Tropical Storms Irene & Lee
DEC Mohawk Update Sept. 13, 2012
Britt E. Westergard, Senior Service Hydrologist National Weather Service, Albany, NY
with Joseph Villani, Hugh Johnson, Vasil Koleci, Kevin Lipton, George Maglaras, Kimberly McMahon, Timothy Scrom, and Thomas Wasula

## Slide 2: Hydrology Topics
Tropical Storm Irene
Outlook / Forecasts
Rainfall
Flood magnitude
Storm surge on Hudson
Operational challenges
Remnants of T.S. Lee
Rainfall
Flood magnitude
Operational challenges
Impacts of Irene & Lee
Post-event activities

## Slide 3: Irene: MMEFS Outlook
http://www.erh.noaa.gov/mmefs/

## Slide 4: Irene: MMEFS Outlook
http://www.erh.noaa.gov/mmefs/

## Slide 5: Irene: Hydrologic Forecasts
Flood watch issued at 4:47 am Friday Aug. 26th
First flash flood warning issued 1:42 am Saturday
Issued river flood warnings (including updated warnings as forecast crests increased in category) for 37 forecast points…flooding occurred at 35
Average lead time from warning to flood stage was 3 hours 12 minutes (FFW LT = 3 hrs)
WIDESPREAD RAINFALL AMOUNTS OF 4 TO 7 INCHES ARE LIKELY.
LOCALIZED AMOUNTS OVER THE HIGHER TERRAIN OF THE
CATSKILLS...BERKSHIRES...LITCHFIELD HILLS AND GREEN MOUNTAINS
COULD REACH 10 INCHES.
IF THIS AMOUNT OF RAIN OCCURS MANY MAIN STEM RIVERS WOULD FLOOD.
FLASH FLOODING MAY ALSO BE A THREAT WHERE HEAVIER RAIN BANDS OCCUR.

## Slide 6: Irene: AHPS forecasts
Sunday
http://water.weather.gov/ahps2/index.php?wfo=aly

## Slide 7: Irene Storm Total Rainfall: Multisensor Estimate
http://www.srh.noaa.gov/ridge2/RFC_Precip/

## Slide 8: Irene: Storm Total Rainfall Interpolated Rain Gages

## Slide 9: Top 5 Wettest Calendar Days at Albany (since 1874)
      5.60" SEP 16 1999 (Floyd)
      4.69" AUG 28 2011 (Irene)
      4.08" AUG 31 1950
      3.50" AUG 28 1971 (Doria)
      3.49" JUL 13 1996 (Bertha)
2011 was the wettest year on record at Albany

## Slide 10: Irene: Tannersville Rainfall
Chart: 
| 40782.822916666664 | 40782.864583333336 | 40782.90625 | 40782.927083333336 | 40782.947916666664 | 40782.989583333336 | 40783.03125 | 40783.072916666664 | 40783.114583333336 | 40783.15625 | 40783.177083333336 | 40783.197916666664 | 40783.239583333336 | 40783.28125 | 40783.322916666664 | 40783.364583333336 | 40783.40625 | 40783.427083333336 | 40783.447916666664 | 40783.489583333336 | 40783.53125 | 40783.572916666664 | 40783.614583333336 | 40783.65625 | 40783.677083333336 | 40783.697916666664 | 40783.739583333336
 | 0 | 0.6 | 0.8 | 0.8 | 0.8 | 1.1 | 1.2 | 1.2 | 1.3 | 1.3 | 1.3 | 1.5 | 2.2 | 2.6 | 3.2 | 4.3 | 5.2 | 5.6 | 6.2 | 7.3 | 8.5 | 9.5 | 10.2 | 10.9 | 11.1 | 11.3 | 11.4
10” in 12 hours
11.6” storm total
New NY State 24 hour rainfall record: 11.6”
Previous record set in 1903 in Central Park
Inches of rainfall

## Slide 11
Flooding at 35 of 44 forecast points.
(5)
(9)
(8)
(13)

## Slide 12: Irene: Storm Surge
Storm Surge = feet above astronomical tide
Storm Tide = feet above datum
(= actual gage elevation if gage datum is zero)
http://hudson.dl.stevens-tech.edu/SSWS/d/index.shtml

## Slide 13: Irene: Storm Surge
@POU: 5.39 ft surge (7.96 tide)
29th highest Irene surge (of 98 meas.)
@ALY: 7.23 ft surge (11.11 ft tide)
16th highest Irene surge
(of 98 meas.)

## Slide 14: Irene: Operational Challenges
Rainfall forecasting
  Placement – 24 hours out, very good
  Timing – reasonable; onset about 6 hours earlier than forecast
  Amount – maximum rainfall in Catskills (18.12”) under-forecast (forecasted max around 10 inches)
HPC Forecast Rainfall Aug 27-29, 2011

## Slide 15: Irene: Operational Challenges
Extreme rates of rise on many rivers
Walloomsac River at Bennington, VT on Aug. 28, exceeded:
- 7 ft flood stage at 10:48am
- 9 ft moderate flood at 11:50am
- 11 ft major flood at 12:46pm
Schoharie Creek at Prattsville, NY on Aug. 28, exceeded: - 12 ft flood stage at 7:02am
- 14 ft moderate flood at 7:36am
- 16 ft major flood at 8:17am

## Slide 16: Irene: Operational Challenges
River gages washed away or damaged:
  Prattsville
  Gilboa Bridge
  Burtonsville
  Poughkeepsie
  Gaylordsville

## Slide 17: Irene: Operational Challenges
Conveying the potential severity of multiple hazards
Communications outages…partners in hardest hit areas
Issues at various locks and dams:
  Misinformation about Gilboa failure
  EAS alert watches for Condition B at several projects taxed the capabilities of our software

## Slide 18: Lee: Track and Rainfall
Notes: http://hydrology.princeton.edu/~luo/research/FORECAST/current.php

## Slide 19: Lee Storm Total Rainfall: Multisensor Estimate
http://www.srh.noaa.gov/ridge2/RFC_Precip/
Moderate to major flood crests:
Major:
  Canajoharie Creek at Canajoharie
  Mohawk River at Utica
  Mohawk River at Little Falls
8 Moderate floods including 3 locations on Schoharie Creek that had just experienced record flooding

## Slide 20: Lee: Operational Challenges
Precipitation forecast uncertainty
  Placement / Timing / Amount
Irene debris
Understanding reports of flooding
Ongoing recovery efforts
Public sensitivity to flooding

## Slide 21: 14 Day Total Rainfall: Multisensor Estimate
http://www.srh.noaa.gov/ridge2/RFC_Precip/
14 days from Thurs. Aug. 25 to Thurs. Sept. 8

## Slide 22
KEY IMPACT STATS | HURRICANE IRENE | TROP. STORM LEE
POWER OUTAGES (PEAK) | 997,000 | 68,000
BRIDGES CLOSED (PEAK) | 24 | 37
ROAD SEGMENTS IMPACTED (PEAK) | 157 | 181
REPORTED SWIFTWATER RESCUES | 150 | 959
EVACUATIONS ORDERED | 370,000+ | 21,000+
Information & photos courtesy of NYS Office of Emergency Management
Notes: Peak outage numbers per PSC. Also, per PSC, there were 11,500 natural gas outages due to Lee and a total of 900,000 telecom outages for Irene/Lee combined.

## Slide 23: Post-Event Activities
Schenectady river gage
  Automated U.S. Geological Survey gage installed January 2011 in coordination w/NYS DEC, Hudson River Environmental Conditions Observing System, Schenectady County EM and Union College
  Flood stage changed January 2012 (223’  220’)
  Impact statement updates
http://www.nws.noaa.gov/om/assessments/index.shtml

## Slide 24
Britt Westergard
britt.westergard@noaa.gov
weather.gov/albany
What a difference a year makes…